## Slide 2
KSAR Hands-on session

## Slide 3
K-SAR Editor Tool Workflow
Legend
K-SAR Editor based on Artop
Development Support Generator
AUTOSAR Platform Editor
Application Source
AUTOSAR
Standard
Application Modeling
ECU Requirement
ECU Platform Editor
Application Editor
Legacy
ODX
AUTOSAR ARXML
DBC
FIBEX
LDF
Import
System
ECU Extract
ECU harmonization
ECU
Parameter Editor
Application SWC
ECU Config Generation and Validation
PDF
BSWMDT
ECU Resource
Build Setup
Editor
Static BSW modules
Generated RTE & BSW source
RTE & BSW Generator
Generated AUTOSAR ARXML
Configuration Management
Build Output
DLT and M&C
Editor
Input/Output Files
Extern
Tool Process
Product Plugin

## Slide 4
K-SAR Embedded and K-SAR Editor Workflow
K-Sar Editor Tool
Generation Tool
Compilation and Linking
Testing
Static
Code
Configuration
Generation
Build
Testing
Generated Code
ECU Extract
Software/System file
Post Build Tool
.C and .H file

## Slide 5: K-SAR Editor– ARTOP Based - layered architecture
ARTOP AUTOSAR (ARTOP User Group)
Rich Client Platform
Eclipse Modeling Framework (EMF)
Eclipse Platform (Eclipse Foundation)
K-SAR Editor (KPIT Technologies Ltd.)
Graphical Modeling Framework (GMF)
EMF Compare
Workbench
JFace
SWT
OSGi
Java VM
Integrated AUTOSAR Tool Environment
Reuse from Artop and Java leads to cost benefit
Better Interoperability of tools
Faster Time to Market, by quick prototyping tool development
Platform Independent Tool installation, Windows or Linux support is available

## Slide 6
Benefits of K-Sar Editor tool on ‘Efficiency’
K-Sar Editor tool supports legacy workflow
Conversion from legacy file format to AUTOSAR format
Standard legacy formats support: DBC, LDF, ODX, FIBEX
(note: These conversion may not be 100%, Customer use case details needed)
Custom plugin can be developed to support Legacy Conversion
K-Sar Editor tool supports flexible workflow
No intermediate file format or data base, pure AUTOSAR standard
BSW Module level arxml configuration can be exported
K-Sar Editor tool support efficient work flow
Harmonization/Automation of BSW software
COM stack including MCAL is configured automatically from ECU extract
OS task and Runnable are automatically configures from SWC import.
DCM and DEM is configured automatically from ODX import
Progressive ECU extracts from OEM and Manual configuration retention
Analysis of difference between two ECU extract
Analysis of difference between two ECU description
Efficiency

## Slide 7: Overview: The software provides a PC based GUI environment for the user to specify the ECU Configuration and generate the ECU Description. This is the proposed tool that shall facilitate user interfaces to specify the ECU Configuration. Parameter Definition File: This is an XML file which shall contain the ECU Configuration Parameter Definition. This file shall provide the structural information on how the ECU Configuration Description and the kind of restrictions that needs to be respected for the individual configuration elements. This file shall form the basis for the tool to create a platform for the respective ECU configuration. Cont….

## Slide 8: ECU Description: This shall be an XML file holding the ECU Configuration. This file shall be generated based on the user configuration specification. The tool shall also provide a provision to import an ECU Configuration. Environment: K-SAR Editor Powered by ARTOP Software runs on Windows. Windows 7 and Windows 8. System Requirements The following are the minimum hardware and software requirements for installation and optimum functioning of K-SAR Editor Powered by ARTOP Software. 32 bit Java Runtime Environment (JRE) Version 6.0 Pentium 4 Processor, Intel core 2 duo, 2.4 GHz, 3 GB minimum RAM Screen Resolution of 1280x768 .

## Slide 9
  K-SAR Editor Powered by ARTOP Software Features

## Slide 10: Creating a New AUTOSAR project Cut, Copy, Paste, Delete, Undo, Redo options Delete of Project, module, container, sub-container, ARPackage, system file Clear Validation Errors Close Project Copy path of Parameter Copy Text of Project name, module name , container name, sub –co ntainer name, ARPackage, System file or any other .arxml file. Create Multiple instances in both ECU and System Editors Create New System Description file Compare ECU Extract Reports Compare with Local History Cont…

## Slide 11: Configure common Value for all the instances Configuring a reference E2E Protection Configuration ECU Configuration Report for CAN, LIN and Flexray ECU Description File Compare Comparison of any two .arxml files (CompareWithEachOther) Configuration of the parameters ECU Extract Report Edit Default Value Exit the workspace Expand and Collapse Export of BSWMD file Export of the project into local system Cont…

## Slide 12: Generate Summary and Detailed report of Module or ARPackage of ECU Global update of the parameter Harmonization of the all the stacks with respect to their input file(s) Help Contents Hex Conversion, Decimal Conversion Import of BSWMD file Import of Custom PDF Import of DBC Import of FIBEX Import of LDF Import of multiple files Import of ODX Import of Software file Cont..

## Slide 13: Import of System file Insert Copy of Container, Sub-Container in ECU configuration and System Configuration editor's Memory Stack Configuration Open existing project into workspace Open with Text Editor Regenerate Handle id(s) Refreshing of Project or workspace RTE ExclusiveAreaMech Automation RTE Mapping Runnable to Task mapping Runtime Validation Save and Save all Search and Replace Cont…..

## Slide 14: Flexray Joblist editor Generate Description file (Module wise and Stack wise) Generate ECU Extract Generate report of the System file Generate Source and Header files Version Details Switch Workspace Sharing a project(s) into SVN Can Hardware Object Mapping

## Slide 15
Can_HW_Object_Mapping

## Slide 20
Data Mapping

## Slide 25
Flexray_Joblist_Editor

## Slide 29
Memory_Stack_Configuration

## Slide 33
Port_Connection (SWConnnectionUtility)

## Slide 37
Runnable_To_Task_Mapping

## Slide 42
DBC_File_Import

## Slide 54
Fibex_File_Import